Force Sensor-Based Weight Measurement System
Using Arduino and LCD Display

---
Introduction
This project develops a force sensor-based weight measurement system. A force sensor detects applied pressure, converting it into a weight value, which is displayed on an LCD screen using Arduino. The system is designed for practical applications like digital weighing.

---
Objectives
To design a weight measurement system using Arduino and a force sensor.
To calibrate the sensor for accurate weight measurement.
To display measured weight on an LCD screen.
To ensure precision and reliability in the system’s output.

---
Figure 1: Circuit Diagram of the system

---
Figure 1: Schematic Diagram of the system

---
     C++ Code
#include <Adafruit_LiquidCrystal.h>
Adafruit_LiquidCrystal lcd(0);
float slope = 0.01;
float offset = 0.0;
void setup()
{
  lcd.begin(16, 2);
  lcd.setBacklight(1);
  lcd.print("Welcome!!!");
  pinMode(A0, INPUT);
}
void loop()
{
  int forceSensorValue = analogRead(A0);
  float voltage = forceSensorValue
* (10.0 / 1023.0);
  float weight = voltage * 10.0;
  lcd.setCursor(0, 1);
  lcd.print("Weight: ");
  lcd.print(weight);
  lcd.print(" g");
}

---
Importance of Sensor Calibration
Ensures accurate, reliable weight readings.
Establishes sensor-weight linearity.
Reduces errors and inconsistencies.
Maintains system accuracy over time.
Inaccuracy: Improper calibration led to inaccurate data in this project.
Callibration

---
Thank you
Md. Abdullah Al Mamun